## Slide 1: In the report about INFN activity
COMMENTS
THGEM is an old detector concept (15-20 years)
Coupling THGEMs and Nanodiamond (ND) photocathode:
  Working down to 140 nm critical because of
    Chromatic dispersion
    Media transparency
    Issues of THGEM outgassing
Why not using MCP coupled to MM (NIMA 535 (2004) 334, NIMA 553 (2005) 76) ?
RECOMMENDATION
new photocathode material is very interesting
  important to understand more thoroughly how the operation at very short wavelengths will actually occur
  Thick GEMs will complicate that picture because of G-10 outgassing water
Summarized in short form

## Slide 2: THE CONTEXT OF THE INFN R&D
Low p (< 5-6 GeV/c, higher ?)
Options
  Proximity focusing RICHes using
    C6F14 (or analogous)
    aerogel
  DIRC & derived detectors
    FDIRC, TOP, TORCH
  Alternative approaches
    New TOF perspectives
    Improved dE/dx by cluster counting in gas
Progress related to numerous new projects:
  Belle-II barrel
  Belle-II forward
  CLAS12
  GlueX
  Panda barrel
  Panda end-caps
  Panda forward
  LHCb-Torch
High p (> 1-4 GeV/c)
Option
  Focusing RICHes with extended gaseous radiator
Presently only 3 running high-p RICHes:
  LHCb (2-counter system)
  NA62 (non h-PID!)
  COMPASS, upgraded : novel MPGD-based PDs
Further future projects:
  Only EIC
Can the radiator be “thinner” to avoid gigantic sizes: (advantages for colliders, also for fixed target)?
namely more detected photons per unit radiator length
proposed so far
  P > 1 atm, proposal for ALICE HMPID upgrade, than abandoned
  Exploit the VUV region with a
  windowless RICH, testbeam @ Fermilab
  Use vacuum-based (visible light) photon detectors
Imaging
Cherenkov
t resolution
~O(10ps)
List from RICH2016
h physics
needs
gaseous PDs
Our focus
IEEE NS 62 (2015) 3256

## Slide 3: THE CONTEXT OF THE INFN R&D
Low p (< 5-6 GeV/c, higher ?)
Options
  Proximity focusing RICHes using
    C6F14 (or analogous)
    aerogel
  DIRC & derived detectors
    FDIRC, TOP, TORCH
  Alternative approaches
    New TOF perspectives
    Improved dE/dx by cluster counting in gas
Progress related to numerous new projects:
  Belle-II barrel
  Belle-II forward
  CLAS12
  GlueX
  Panda barrel
  Panda end-caps
  Panda forward
  LHCb-Torch
High p (> 1-4 GeV/c)
Option
  Focusing RICHes with extended gaseous radiator
Presently only 3 running high-p RICHes:
  LHCb (2-counter system)
  NA62 (non h-PID!)
  COMPASS, upgraded : novel MPGD-based PDs
Further future projects:
  Only EIC
Can the radiator be “thinner” to avoid gigantic sizes: (advantages for colliders, also for fixed target)?
namely more detected photons per unit radiator length
proposed so far
  P > 1 atm, proposal for ALICE HMPID upgrade, than abandoned
  Exploit the VUV region with a
  windowless RICH, testbeam @ Fermilab
  Use vacuum-based (visible light) photon detectors
Imaging
Cherenkov
t resolution
~O(10ps)
List from RICH2016
h physics
needs
gaseous PDs
Our focus
IEEE NS 62 (2015) 3256
World-wide activity ongoing for h PID at low momenta (interest of a wide scientific community) :
a suitable and convincing approach for experiments at EIC can be found within this context
Very limited recent activity for h PID at high momenta (in the next years only R&D for EIC foreseen): our focus is here
Extra difficulty: compress the radiator length to match the requirements of a collider setup
No consistent detector concept existing yet; most likely upgraded gaseous photon detectors have to be used (central brick for a RICH) : this is the goal of the present stage of our R&D (later: move to a complete detector concept)

## Slide 4: About THGEMS
YES, the concept is old
(reminder: THGEM also called LEM in literature)
So far used in a single experiment: novel photon detectors of COMPASS RICH-1
  it took years to understand them and reach production technique maturity (R&D for COMPASS: 7 years)
THGEM outgassing
  important ingredient: bake them to complete epoxy curing (not the case for standard PCB production)
  Form direct experience:
  Vacuum level while pumping
  in order to prepare
  for CsI coating
THGEM introduced in // by different groups:
L. Periale et al., NIM A478 (2002) 377
P. Jeanneret, PhD thesis, Neuchatel U., 2001
P.S. Barbeau et al., IEEE NS50 (2003) 1285
R. Chechik et al., NIMA 535 (2004) 303
6 days
Reference board, NO HOLES !
THGEM
Vacuum level (mbar)
1x10-7 2.51x10-6
No extra outgassing from
the 325,000 holes in the THGEM !

## Slide 5: About OPERATION IN THE FAR UV DOMAIN
COMPASS RICH-1, gas transparency
gas cleaning by on-line filters,
separate functions:
  Cu catalyst, ~ 400C for O2
  5A molecular sieve, ~ 100C for H2O
transmission
through 1,87 m,
corresponding to:
H2O: ~1 ppm,
O2: ~3 ppm
typical
wavelength (nm)
transmission
0 0.2 0.4 0.6 0.8 1
160 170 180 190 200 210
CsI QE
quartz
(n-1) r.m.s (assuming Frank and Tamm):
30×10−6 < 46×10−6
PHENIX HBD
CsI + GEMs
CsI gasous sensors used
in several Cherenkov detectors
Refractvie index
Chromatic dispersion depends also on the wavelength acceptance range
FACTS

## Slide 6: About OPERATION IN THE FAR UV DOMAIN
QE is similar in ND and CsI
ND is expected to be by far more robust
L.Velardi, A.Valentini, G.Cicala al.,
Diamond & Related Materials 76 (2017) 1
47 % (!)
A RICH prototype has explored the very far UV domain
  in a windowless RICH using CF4
  Using quintuple GEMs and CsI
  by using a thin-film mirror (25 nm MgF2), reflecting in a limited range around 120 nm
IEEE NS 62 (2015) 3256

## Slide 7: MCP coupled to MM
Most likely interesting, nevertheless a completely different approach that would require restarting from scratch …
At the moment, not considered